## Slide 1: WATER ALLOCATION TOOL SESSION 1 (repeat)
  Introduction / Background
  Water Allocation Tool / DWRAT Framework
  Q & A / Discussion

## Slide 2: UPCOMING PRESENTATIONS & TRAINING SESSIONS
1 – background, context, introduction, discussion
2 – DWRAT equations, input data, general workflow
3.A – presentation of output & related data
3.B – brainstorming metrics, analyses, discussion
4.A – presentation of python code, downloading & running
script from command line
4.B – scenario development, input files, data sources
5.A – use of main and ancillary python scripts, data
processing
5.B – programming continued, building the project folder

## Slide 3: WATER ALLOCATION TOOL
A need for a formal procedure and tools to evaluate water availability that are:
  Quantitative
  Transparent
  Open source
  Inexpensive to implement
  Easy to learn

## Slide 4: WATER ALLOCATION TOOL EQUATIONS

## Slide 5: WATER ALLOCATION
The process of distributing water supplies to various uses when there is a shortfall.
If there is no shortage, all uses could receive an allocation of the full amount needed.

## Slide 6: Appropriative model results
Goal:
  Minimize penalties
Some results:
  User 1 gets full allocation
  Users 3 and 4 run out of water
  Users 10 and 11 receive no allocation
Users | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Demand: | 7 | 4 | 8 | 8 | 8 | 4 | 3 | 9 | 9 | 7 | 10
Allocation: | 7.0 | 4.0 | 5.6 | 5.6 | 8.0 | 4.0 | 3.0 | 4.4 | 3.2 | 0.0 | 0.0
Shortage: | 0.0 | 0.0 | 2.4 | 2.4 | 0.0 | 0.0 | 0.0 | 4.6 | 5.8 | 7.0 | 10.0
Notes: User 1 receives full allocation, runs out of right before runs out of water
Users 3 and 4 have high priority, but there just isn’t enough water available so they experience shortage. Run out of water before they run out of right

## Slide 7: REASONS TO ALLOCATE WATER
To manage streams during periods of water shortage (i.e. curtail) in real time
To evaluate instream flow management scenarios and regulatory approaches

## Slide 8: REASONS TO ALLOCATE WATER
Determining instream flow at a point in time and space requires knowing both:
  flow
  diversions
(or a stream gage)
Hydrology model flows are generally unimpaired

## Slide 9: HOW TO ALLOCATE WATER ?
  A legal system of water rights and environmental protections
  Other ways:
    First come first served
    Auctions
    Lottery
    By use value
    Through corruption ?

## Slide 10: WHY ALLOCATE WATER ?
State Water Board Mission Statement
  To preserve, enhance, and restore the quality of California's water resources and drinking water for the protection of the environment, public health, and all beneficial uses, and to ensure proper water resource allocation and efficient use, for the benefit of present and future generations.
California Constitution Article X Section 2
  general welfare requires that the water resources of the State be put to beneficial use to the fullest extent of which they are capable…
Water Rights Mission Statement
  Our Mission is to establish and maintain a stable system of water rights in California to best develop, conserve, and utilize in the public interest the water resources of the State while protecting vested rights, water quality and the environment

## Slide 11: HOW DOES CALIFORNIA ALLOCATE WATER ?
  Maximize beneficial use of water, subject to environmental protection, in accordance with water rights and California state law

## Slide 12: OPTIMIZATION
determining the action that best achieves a desired goal or objective.
This means finding the action that optimizes (that is, maximizes or minimizes) the value of an objective function.

## Slide 13: OPTIMIZATION PROBLEMS
THREE ELEMENTS IN COMMON
  Objective function
  Decision variables
  Constraints

## Slide 14: OPTIMIZATION PROBLEMS OBJECTIVE FUNCTIONS
objective functions:
  A quantification of the management goal in terms of the decision variables
  (in linear programming) the function that it is desired to maximize or minimize.

## Slide 15: OPTIMIZATION PROBLEMS DECISION VARIABLES
decision variables:
  Values or allocations that need to be set to find the optimum of the objective function

## Slide 16: OPTIMIZATION PROBLEMS CONSTRAINTS
Constraints:
  A set of equations or requirements that restrict the values of the decision variables

## Slide 17: EXAMPLE OPTIMIZATION PROBLEM
What is the minimum cost to enclose a 400 sq-ft garden if Sam’s neighbor is paying half of the shared side?
https://www.matheno.com/calculus-1/optimization/garden-fence/

## Slide 18: DECISION VARIABLES
  x (width)
  y (length)

## Slide 19: CONSTRAINTS
x * y = 400 square feet
Solve or y in terms of x:
y = 400 / x

## Slide 20: OBJECTIVE FUNCTION
Minimize C, (cost) as a function of x

## Slide 21: FINDING OPTIMUM
Solving for (x, y) that minimizes cost requires lots of calculus
And real problems have 100s -1000s of decision variables
We need a Solver program

## Slide 22: MS EXCEL SOLVER add-in

## Slide 23: PuLP 2.0
Open source Python package for Linear Program modeling
  Integrates with many available solvers
  Used by UC Davis
  Able to handle 1000s of decision variables vs. MS Excel maximum of 200

## Slide 24: WATER ALLOCATION TOOL
A need for a formal procedure and tools to evaluate water availability that are:
  Quantitative
  Transparent
  Open source
  Inexpensive to implement
  Easy to learn

## Slide 25: DWRAT FRAMEWORK
Integrated set of mathematical equations that describe
  water availability
  instream flow requirements
  and California water rights
These equations can be solved for an optimal water allocation among diverters given
  basin flows
  water demand
  priority

## Slide 26: TEN EQUATIONS

## Slide 27: ASSUMPTIONS
Every user has access to all basin flow
All water use is 100% consumptive – no return flows
No losses to groundwater or evaporation
Flow is available to the whole network at each time step

## Slide 28: DATA INPUTS
SUBBASINS:
  inflow in units volume / time
  downstream subbasin
USERS:
  demand in units volume / time
  location
  priority
Optionally: e-flows, buffer, health & safety

## Slide 29: VARIABLE DEFINITIONS
i : user subscript
k : basin subscript
Pk : basin proportion
Ai : user allocation
ui : user demand
vk : basin inflow
ek : environmental flow
wk : basin downstream cost
pi : appropriative user priority

## Slide 30: RIPARIAN DECISION VARIABLES Equations (1) & (2)
Basin proportions of demand allocated to riparian users:
Actual allocation is determined by proportions

## Slide 31: APPROPRIATIVE DECISION VARIABLES Equation (8)
Actual allocation for each appropriative user

## Slide 32: MASS BALANCE CONSTRAINT Equation (3)
RIPARIAN

## Slide 33: MASS BALANCE CONSTRAINT Equation (9)
APPROPRIATIVE

## Slide 34: RIPARIAN LEGAL CONSTRAINTS Equations (5) & (6)
Shared shortage:
However:

## Slide 35: APPROPRIATIVE LEGAL CONSTRAINTS
Seniority system shortage is minimized according to seniority:
Shortage is scaled in the objective function by the inverse of the priority aka (shortage penalty)

## Slide 36: RIPARIAN OBJECTIVE FUNCTION Equations (4) & (7)
Maximize riparian allocations:

## Slide 37: APPROPRIATIVE OBJECTIVE FUNCTION Equation (10)
Maximize appropriative allocations by seniority:

## Slide 38: OUTPUT
APPROPRIATIVE USERS
  flow allocation in units volume / time
RIPARIAN USERS
  basin proportion of demand

## Slide 39: NOTES
Resulting allocations are a best estimate
Only as accurate as the input data
Will require further testing, and adaptation to specific watersheds

## Slide 40: EXAMPLE MODEL
8 Basin 11 user toy model
Two scenarios:
  All users riparian, equal priority
  All users appropriative, priority by seniority
Local inflow of 7 for each watershed, 20% reserved for environmental flow
User: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Demand: | 7 | 4 | 8 | 8 | 8 | 4 | 3 | 9 | 9 | 7 | 10

## Slide 41: QUESTIONS ?

## Slide 42: EXAMPLE MODEL
8 Basin 11 user toy model
Two scenarios:
  All users riparian, equal priority
  All users appropriative, priority by seniority
Local inflow of 7 for each watershed, 20% reserved for environmental flow
User: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Demand: | 7 | 4 | 8 | 8 | 8 | 4 | 3 | 9 | 9 | 7 | 10

## Slide 43: BASIN DATASETS

## Slide 44: USER DATASETS

## Slide 45: CONNECTIVITY MATRIX
A value of 1 indicates user (column) is upstream of basin outlet (row)
Used for implementation of mass balance constraints
Generated with GIS in larger river basins
 |  | Users |  |  |  |  |  |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Basins | A |  |  |  | 1 |  |  |  |  |  |  | 1
 | B |  |  | 1 |  |  |  |  |  |  |  | 
 | C |  | 1 | 1 | 1 |  |  |  |  |  |  | 1
 | D |  |  |  |  |  |  | 1 |  |  |  | 
 | E |  | 1 | 1 | 1 |  | 1 | 1 | 1 |  |  | 1
 | F | 1 | 1 | 1 | 1 |  | 1 | 1 | 1 |  | 1 | 1
 | G |  |  |  |  |  |  |  |  | 1 |  | 
 | H | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 46: RIPARIAN MODEL RESULTS
Goal: Maximize total allocations with equitable distribution of shortage
Sensitivity analysis:
  Upstream demand exceeds availability at points with red circles
User: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Demand: | 7.0 | 4.0 | 8.0 | 8.0 | 8.0 | 4.0 | 3.0 | 9.0 | 9.0 | 7.0 | 10.0
Allocation: | 4.7 | 2.7 | 5.3 | 2.5 | 5.6 | 2.7 | 2.0 | 6.0 | 5.6 | 4.7 | 3.1
P: | 0.67 | 0.67 | 0.67 | 0.31 | 0.70 | 0.67 | 0.67 | 0.67 | 0.62 | 0.67 | 0.31
Shortage: | 2.34 | 1.34 | 2.67 | 5.51 | 2.41 | 1.34 | 1.00 | 3.01 | 3.41 | 2.34 | 6.89

## Slide 47: RIPARIAN MODEL RESULTS
Curtailments in A
- Demand exceeds availability (FLOW LIMITED)
User: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Demand: | 7.0 | 4.0 | 8.0 | 8.0 | 8.0 | 4.0 | 3.0 | 9.0 | 9.0 | 7.0 | 10.0
Allocation: | 4.7 | 2.7 | 5.3 | 2.5 | 5.6 | 2.7 | 2.0 | 6.0 | 5.6 | 4.7 | 3.1
P: | 0.67 | 0.67 | 0.67 | 0.31 | 0.70 | 0.67 | 0.67 | 0.67 | 0.62 | 0.67 | 0.31
Shortage: | 2.34 | 1.34 | 2.67 | 5.51 | 2.41 | 1.34 | 1.00 | 3.01 | 3.41 | 2.34 | 6.89

## Slide 48: RIPARIAN MODEL RESULTS
User: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Demand: | 7.0 | 4.0 | 8.0 | 8.0 | 8.0 | 4.0 | 3.0 | 9.0 | 9.0 | 7.0 | 10.0
Allocation: | 4.7 | 2.7 | 5.3 | 2.5 | 5.6 | 2.7 | 2.0 | 6.0 | 5.6 | 4.7 | 3.1
P: | 0.67 | 0.67 | 0.67 | 0.31 | 0.70 | 0.67 | 0.67 | 0.67 | 0.62 | 0.67 | 0.31
Shortage: | 2.34 | 1.34 | 2.67 | 5.51 | 2.41 | 1.34 | 1.00 | 3.01 | 3.41 | 2.34 | 6.89
Curtailments in B
Availability exceeds demand
(DOWNSTREAM DEMAND LIMITED)
Downstream users in F have excessive demand
B is curtailed so downstream users experience less shortage

## Slide 49: RIPARIAN ALLOCATIONS
From Water rights curtailments for drought in California: Method and Eel River Application
Benjamin Lord’s Master Thesis 2015

## Slide 50: Appropriative model results
Goal:
  Minimize penalties
Some results:
  User 1 gets full allocation
  Users 3 and 4 run out of water
  Users 10 and 11 receive no allocation
Users | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Demand: | 7 | 4 | 8 | 8 | 8 | 4 | 3 | 9 | 9 | 7 | 10
Allocation: | 7.0 | 4.0 | 5.6 | 5.6 | 8.0 | 4.0 | 3.0 | 4.4 | 3.2 | 0.0 | 0.0
Shortage: | 0.0 | 0.0 | 2.4 | 2.4 | 0.0 | 0.0 | 0.0 | 4.6 | 5.8 | 7.0 | 10.0
Notes: User 1 receives full allocation, runs out of right before runs out of water
Users 3 and 4 have high priority, but there just isn’t enough water available so they experience shortage. Run out of water before they run out of right

## Slide 51: UPCOMING PRESENTATIONS & TRAINING SESSIONS
1 – background, context, introduction, discussion (REPEAT)
2 – DWRAT equations, input data, general workflow
3.A – presentation of output & related data
3.B – brainstorming metrics, analyses, discussion
4.A – presentation of python code, downloading & running
script from command line
4.B – scenario development, input files, data sources
5.A – use of main and ancillary python scripts, data
processing
5.B – programming continued, building the project folder

## Slide 52: SESSION TWO
2 – DWRAT equations in depth, input data, data processing, general workflow, review, discussion.