## Slide 1: WATER ALLOCATION TOOL SESSION 2
  Review Session 1
  Connectivity matrices
  Linear programming (LP)
  Linear algebra
  Variables
  DWRAT equations & calculations
  Q & A / Discussion

## Slide 2: TRAINING SESSION SERIES
1 – background, context, introduction, discussion
2 – DWRAT equations, input data, general workflow
3.A – presentation of input, output & related data
3.B – brainstorming metrics, analyses, discussion
4.A – presentation of python code, downloading & running
script from command line
4.B – scenario development, input files, data sources
5.A – use of main and ancillary python scripts, data
processing
5.B – programming continued, building the project folder

## Slide 3: DWRAT FRAMEWORK
Integrated set of mathematical equations that describe
  water availability
  instream flow requirements
  and California water rights
These equations can be solved for an optimal water allocation among diverters given
  basin flows
  water demand
  priority

## Slide 4: WATER ALLOCATION
The process of distributing water supplies to various uses when there is a shortfall.
If there is no shortage, all uses could receive an allocation of the full amount needed.

## Slide 5: REASONS TO ALLOCATE WATER
To manage streams during periods of water shortage (i.e. curtail) in real time
To evaluate instream flow management scenarios and regulatory approaches

## Slide 6: OPTIMIZATION
determining the action that best achieves a desired goal or objective.
This means finding the action that optimizes (that is, maximizes or minimizes) the value of an objective function.

## Slide 7: OPTIMIZATION PROBLEMS OBJECTIVE FUNCTIONS
objective functions:
  A quantification of the management goal in terms of the decision variables
  (in linear programming) the function that it is desired to maximize or minimize.

## Slide 8: OPTIMIZATION PROBLEMS - DECISION VARIABLES
decision variables:
  Values or allocations that need to be set to find the optimum of the objective function

## Slide 9: OPTIMIZATION PROBLEMS - CONSTRAINTS
Constraints:
  A set of equations or requirements that restrict the values of the decision variables

## Slide 10: WATER ALLOCATION TOOL EQUATIONS

## Slide 11: EXAMPLE MODEL
8 Basin 11 user toy model
Two scenarios:
  All users riparian, equal priority
  All users appropriative, priority by seniority
Local inflow of 7 for each watershed, 20% reserved for environmental flow = 5.6
User: | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Demand: | 7 | 4 | 8 | 8 | 8 | 4 | 3 | 9 | 9 | 7 | 10

## Slide 12: SOME NOTATION
This is formal proof stuff
  …
  …

## Slide 13: MOTIVATION

## Slide 14: EQUATION ONE
,
  (last time: )
  multiply each user’s demand by the basin proportion in the basin where they reside
  need to specify basin location of each user with a matrix…

## Slide 15: WHAT IS A MATRIX ?
A rectangular array of numerical quantities arranged in a systematic fashion into rows and columns
Matrices describe aspects of phenomena which are inter-related in some manner
E.g. user & basin location
Vectors are matrices having a single column or row

## Slide 16: BASIN CONNECTIVITY MATRIX
Every basin is upstream of itself
Zeros are removed for legibility
Read from left to right, a (1) in a column indicates that the basin is upstream of that row basin.
A, B, and C are upstream of C

## Slide 17: LINEAR PROGRAM

## Slide 18: GEORGE B. DANTZIG (1914 – 2005)
The “real” Will Hunting
  Inventor of linear programming (LP) and Simplex Method
Revolutionized the way government and private enterprise planned, scheduled and optimized operations
Simplex method
  algo for solving LP problems (1947)
  one of the earliest,
  most important, and
  widely used algorithms of 20th century

## Slide 19: LINEAR PROGRAMMING
  A technique for optimization of a linear objective function, subject to linear equality and inequality constraints.

## Slide 20: LINEAR ALBEGRA
  If linear algebra grew out of the solution of systems of linear equations, then linear programming grew out of attempts to solve systems of linear inequalities, allowing one to optimize linear functions subject to constraints expressed as inequalities

## Slide 21: LINEAR ALBEGRA
  Is using arithmetic on columns of numbers called vectors, and arrays of numbers called matrices, to create new columns and arrays of numbers

## Slide 22: MATRIX TRANSPOSITON

## Slide 23: DOT PRODUCT

## Slide 24: MATRIX MULTIPLICATION

## Slide 25: MATRIX MULTIPLICATION

## Slide 26: MATRIX MULTIPLICATION

## Slide 27: MATRIX MULTIPLICATION

## Slide 28: BASIN CONNECTIVITY MATRIX
Every basin is upstream of itself
Zeros are removed for legibility
Read from left to right, a (1) in a column indicates that the basin is upstream of that row basin.
A, B, and C are upstream of C

## Slide 29: USER LOCATION MATRIX
Zeros have been removed…
All users have a 1 indicating their basin location

## Slide 30: USER CONNECTIVITY MATRIX
Read from left to right, a 1 in a column indicates that the user is upstream of the row basin.
Users 2, 3, 4, and 11 are upstream of basin C

## Slide 31: BASIN VARIABLE DEFINITIONS
P : basin proportion
v : basin inflow
e : environmental flow
w : basin downstream cost

## Slide 32: USER VARIABLE DEFINITIONS
A : user allocation
u : user demand
p : appropriative user priority

## Slide 33: INPUT VARIABLES
Formulation variables:
u : user demand
v : basin inflow
e : environmental flow
Other required inputs:
  user priority rank
  basin downstream basin, i.e. “flows to”

## Slide 34: OUTPUT VARIABLES
P : basin proportion
A : user allocation (appropriative)

## Slide 35: DERIVED VARIABLES
p : appropriative user weight
A : user flow allocation (riparian, EQUATION 1)
w : basin downstream penalty (cost, EQUATION 6)

## Slide 36: PRELIMINARY CALCULATIONS
AVAILABLE FLOW
UPSTREAM DEMAND

## Slide 37: BASIN CONNECTIVITY MATRIX
Every basin is upstream of itself
Zeros are removed for legibility
Read from left to right, a (1) in a column indicates that the basin is upstream of that row basin.
A, B, and C are upstream of C

## Slide 38: AVAILABLE BASIN FLOW v
Matrix operations:
upstream connectivity matrix * net flow
(k x k) ∙ (k x 1) = k x 1 list of available net basin flows
∙ =

## Slide 39: AVAILABLE BASIN FLOW v
=
=
∙

## Slide 40: USER CONNECTIVITY MATRIX
Read from left to right, a 1 in a column indicates that the user is upstream of the row basin.
Users 2, 3, 4, and 11 are upstream of basin C

## Slide 41: UPSTREAM BASIN DEMAND u
Basin Demand is the sum of user demand upstream of each basin. k x i user connectivity matrix * i x 1 list of user demand = k x 1 basin demand
=
∙

## Slide 42: UPSTREAM BASIN DEMAND u
=
=
∙

## Slide 43: TOTAL BASIN DEMAND – NOT UPSTREAM BASIN DEMAND
  [[0, 0, 0, 1, 0, 0, 0, 0, 0, 0, 1]
  [0, 0, 1, 0, 0, 0, 0, 0, 0, 0, 0]
  [0, 1, 0, 0, 0, 0, 0, 0, 0, 0, 0]
  [0, 0, 0, 0, 0, 0, 1, 0, 0, 0, 0]
  [0, 0, 0, 0, 0, 1, 0, 1, 0, 0, 0]
  [1, 0, 0, 0, 0, 0, 0, 0, 0, 1, 0]
  [0, 0, 0, 0, 0, 0, 0, 0, 1, 0, 0]
  [0, 0, 0, 0, 1, 0, 0, 0, 0, 0, 0]]
∙
∙

## Slide 44: EQUATION ONE
,

## Slide 45: EQUATION THREE
The sum of user allocations in each basin is less than or equal to available flow.
Already have a x 1 column matrix for
This is constrained to be ≤ the k x 1 column matrix of available flows calculated above.

## Slide 46: EQUATION SIX
The downstream penalty is simply the ratio between the number of users upstream of basin k, and the total number of users in the system.

## Slide 47: USERS UPSTREAM OF basin k
(The user connectivity matrix)

## Slide 48: EQUATION SIX
downstream_penalty_list = np.divide(np.sum(riparian_user_connectivity_matrix, 1),
np.count_nonzero(rip_users))

## Slide 49: EQUATION SEVEN
We already have both these quantities.

## Slide 50: EQUATION TWO
0 ≤
No calculations Required. Just a constraint.

## Slide 51: EQUATION FIVE
There are different ways of specifying this constraint.

## Slide 52: EQUATION FOUR
We already have these quantities

## Slide 53: BASIN ALLOCATION
This is simple multiplication
(element by element)
Riparian proportion allocation * (basin demand
*
We already have most of the quantities we need

## Slide 54: APPROPRIATIVE MODULE
We already have most of the quantities we need

## Slide 55: AVAILABLE (UNALLOCATED) BASIN FLOW v
∙ =

## Slide 56: EQUATION EIGHT
0 ≤
No calculations Required. Just a constraint.

## Slide 57: EQUATION NINE
The sum of appropriative user allocations in each basin is less than or equal to (original) available flow less riparian upstream allocations.
is an x 1 column matrix of decision variables
This is constrained within each basin to be ≤ the x 1 column matrix of available flows calculated above.

## Slide 58: EQUATION TEN
This is just element-wise arithmetic

## Slide 59: DEMONSTRATION

## Slide 60: QUESTIONS ?

## Slide 61: UPCOMING PRESENTATIONS & TRAINING SESSIONS
3.A – presentation of input, output & related data
3.B – brainstorming metrics, analyses, discussion
4.A – presentation of python code, downloading & running
script from command line
4.B – scenario development, input files, data sources
5.A – use of main and ancillary python scripts, data
processing
5.B – programming continued, building the project folder

## Slide 62: SESSION THREE A/B
3.A – presentation of input, output & related data, discussion
3.B – brainstorming metrics, analyses, discussion